## Slide 1: Science Assessment to Support an Illinois Nutrient Loss Reduction Strategy
Mark David, Greg McIsaac, George Czapar, Gary Schnitkey, Corey Mitchell
University of Illinois at Urbana-Champaign
November 13, 2013
11-08-12

## Slide 2: Riverine N and P Fluxes
 | Water | Nitrate-N | Total N | DRP | Total P
 | 1012 ft3 yr-1 | million lb N or P yr-1 |  |  | 
David & Gentry (2000) | 1.6 |  | 538 |  | 31.3
1980-1996 | 1.70 | 404 | 527 | 15.4 | 34.0
1997-2011 | 1.72 | 410 | 536 | 18.5 | 37.5
Urban runoff |  | 6.0 | 8.3 |  | 1.5
Point sources |  | 75.2 | 87.3 |  | 18.1
 |  | Percent of 1997-2011 load |  |  | 
Point sources |  | 18.4 | 16.3 |  | 48
David & Gentry (2000) |  |  | 16 |  | 47

## Slide 3: Illinois Nutrient Sources
Chart: 
| Urban runoff | Point sources | Agricultural
Total N | 1.5505 | 16.2873 | 82.1622
Chart: 
| Urban runoff | Point sources | Agricultural
Nitrate-N | 1.4754 | 18.3415 | 80.1831
Total N | 1.5505 | 16.2873 | 82.1622
Chart: 
| Urban runoff | Point sources | Agricultural
Total P | 3.979 | 48.2667 | 47.7543

## Slide 4: Point and agricultural sources (1997-2011)

## Slide 8: Nitrate-N and Total P Targets
Red line is target, purple is average 1997 to 2011

## Slide 9: Point Source P Estimates
Point Source Limit (mg P/L) | million lb of P reduced | % of target (18.8 million lb P)
All majors to 1 mg/L standard (0.7 mg P/L actual) | 10.4 | 55
Top 20 majors to 0.7 | 6.1 | 32
Top 30 majors to 0.7 | 7.0 | 37
Top 50 majors to 0.7 | 7.8 | 41
All majors to 0.3 | 13.1 | 70
Top 20 majors to 0.3 | 8.0 | 42
Top 30 majors to 0.3 | 8.9 | 47
Top 50 majors to 0.3 | 9.9 | 52
Total P from point sources currently ~18.1 million lb P per year

## Slide 10: Possible intermediate reduction goal
30% total P reduction by 2025
  top 50 majors reduce total P to 0.7 mg P/L (21%)
  buffers and cover crops (9%)
20% nitrate-N reduction by 2025
  fertilizer timing, cover crops, buffers, and bioreactors (20%)
to Gulf of Mexico

## Slide 12: Nitrate Yield by MLRA
Combined MLRA | Description | Drained cropland (acres) | Nitrate-N yield per row crop acre (lb N/acre/yr) | Nitrate-N yield per tile drained acre (lb N/acre/yr) | Nitrate-N yield from non-tiled land (lb N/acre/yr)
MLRA 1 | Northern Illinois drift plain | 288,491 | 20.4 | 43 | 6.6
MLRA 2 | Northeastern Illinois heavy till plain | 2,063,695 | 25.0 | 29 | 10.8
MLRA 3 | Northern Mississippi Valley | 20,942 | 31.3 |  | 31.3
MLRA 4 | Deep loess and drift | 5,437,807 | 19.6 | 26 | 9.9
MLRA 5 | Claypan | 310,087 | 6.6 |  | 6.6
MLRA 6 | Thin loess and till | 226,971 | 7.4 | 30 | 3.5
MLRA 7 | Central Mississippi Valley, Northern Part | 1,284,588 | 24.5 | 46 | 11.8
MLRA 8 | Sandstone and shale hills and valleys | 49,565 | 3.9 |  | 3.9
MLRA 9 | Central Mississippi Valley, Western Part | 23,769 | 4.0 |  | 4.0

## Slide 13: Cost analysis
Gary Schnitkey
  agricultural costs per acre
Mark David
  point source costs
  N loss reduction costs
Greg McIsaac
  P loss reduction costs

## Slide 14: Agricultural Cost Estimates
No changes in corn and soybean yields across scenarios
No reduction in nitrogen application rates with timing changes
Up front costs amortized over 20 years at 6% interest rate

## Slide 15: Costs per acre
 | Practice/Scenario | Cost Per Acre | Notes
 | Reducing N rate from background to the MRTN (10% of acres) | -$8 | Reduce N rates (20 pounds)
 | Nitrification inhibitor with all fall applied fertilizer on tile-drained corn acres | $7 | Cost of inhibitor
 | Split (50%) fall and spring (50%) on tile-drained corn acres | $17 | Additional field pass, switch to N solutions
 | Fall to spring on tile-drained corn acres | $18 | Switch to N solutions, higher ammonia price, additional application costs
 | Cover crops on all corn/soybean tile-drained acres | $29 | Aerial applications of cereal rye
 | Cover crops on all corn/soybean non-tiled acres | $29 | Aerial applications of cereal rye
 | Bioreactors on 50% of tile-drained land | $17 | Upfront costs of $133 per acre
 | Wetlands on 25% of tile-drained land | $60 | 5% of farmland out of production Major cost is land ($11,000)
 | Buffers on all applicable crop land (reduction only for water that interacts with active area) | $294 per buffer acre | Land costs plus $50 planting, $10 yearly maintenance
 | Perennial/energy crops equal to pasture/hay acreage from 1987 | $86 | Less profit compared to corn-soybean rotation
 | Perennial/energy crops on 10% of tile-drained land | $86 | Less profit compared to corn-soybean rotation
Edge-of-field
Land use change
In-field

## Slide 16: P Reduction Practices
Reduce tillage: -$16 per acre
  One less field pass
Eliminate P application for six years: -$15 per acre
  Eliminate 6 years of applications, spread over 20 years to draw down P reserves
Incorporate P: $6 per acre
  Additional application costs

## Slide 17: Point Source Costs
dependent on size of facility
  costs >>>> for smaller STP’s (< 1-2 MGD)
great variability among STP’s
used data from:
  North Shore Sanitary District
    three plant cost analysis
  USEPA 2008 Municipal Nutrient Removal Technologies report
    eight plant case study
more data to come, cost per lb likely to increase

## Slide 18: Point Source Cost Summary (more estimates to be added)
Median $2.92/lb P $1.72 lb/N

## Slide 19: Example Statewide Results for N
 | Practice/Scenario | Nitrate-N reduction per acre (%) | Nitrate-N reduced (million lb N) | Nitrate-N Reduction % (from baseline) | Cost ($/lb N removed)
 | Baseline |  | 410 |  | 
 | Reducing N rate from background to the MRTN (10% of acres) | 10 | 2.3 | 0.6 | -4.25
 | Nitrification inhibitor with all fall applied fertilizer on tile-drained corn acres | 10 | 4.3 | 1.0 | 2.33
 | Split (50%) fall and spring (50%) on tile-drained corn acres | 7.5 to 10 | 13 | 3.1 | 6.22
 | Fall to spring on tile-drained corn acres | 15 to 20 | 26 | 6.4 | 3.17
 | Cover crops on all corn/soybean tile-drained acres | 30 | 84 | 20.5 | 3.21
 | Cover crops on all corn/soybean non-tiled acres | 30 | 32 | 7.9 | 11.33
 | Bioreactors on 50% of tile-drained land | 40 | 56 | 13.6 | 1.38
 | Wetlands on 25% of tile-drained land | 40 | 35 | 8.5 | 4.05
 | Buffers on all applicable crop land (reduction only for water that interacts with active area) | 90 | 36 | 8.7 | 1.63
 | Perennial/energy crops equal to pasture/hay acreage from 1987 | 90 | 10 | 2.5 | 9.72
 | Perennial/energy crops on 10% of tile-drained land | 90 | 25 | 6.1 | 3.18
 | Point source reduction to 10 mg nitrate-N/L |  | 14 | 3.4 | 1.72
 | Point source reduction in N due to biological nutrient removal for P |  | 8 | 1.8 | 
Point source
Edge-of-field
Land use change
In-field

## Slide 20: Example Statewide Results for P
 | Practice/Scenario | Total P reduction per acre (%) | Total P reduced (million lb P) | Total P Reduction % (from baseline) | Cost ($/lb P removed)
 | Baseline |  | 37.5 |  | 
 | Convert 1.8 million acres of conventional till eroding >T to reduced, mulch or no-till | 50 | 1.8 | 5.0 | -16.60
 | P rate reduction on fields with soil test P above the recommended maintenance level | 7 | 1.9 | 5.0 | -97.50
 | Cover crops on all corn/soybean acres | 30 | 5.7 | 15.2 | 109.40
 | Cover crops on 1.6 million acres eroding>T currently in reduced, mulch or no-till | 50 | 1.9 | 5.0 | 24.50
 | Incorporation of all P fertilizers | 25 | Unknown area | Unknown | 
 | Wetlands on 25% of tile-drained land | 0 | 0 | 0.0 | 
 | Buffers on all applicable crop land | 25-50 | 4.8 | 12.9 | 11.97
 | Perennial/energy crops equal to pasture/hay acreage from 1987 | 90 | 1.0 | 2.7 | 93.59
 | Perennial/energy crops on 1.6 million acres>T currently in reduced, mulch or no-till | 90 | 3.5 | 9.0 | 40.40
 | Perennial/energy crops on 10% of tile-drained land | 50 | 0.3 | 0.8 | 250.07
 | Point source reduction to 0.5 mg total P/L |  | 11.7 | 31.2 | 2.92
Point source
Edge-of-field
Land use change
In-field

## Slide 21: University of Illinois Science Team Website
http://biogeochemistry.nres.illinois.edu/Biogeochem_lab/Illinois_Science_Assessment.html

## Slide 22: Iowa Costs

## Slide 23: Overall Comparison of Nitrate-N Practices
 | Nitrate-N Reduction | Cost of N Reduction | Other Benefits (Ecosystem Services)
Practice/Scenario | % (from baseline) | ($/lb) | 
Reducing nitrogen application rate from background to the MRTN | 9 | -0.58 | 
Cover crops (rye) on ALL CS and CC acres | 28 | 5.96 | ++
Install Wetlands to treat 45% of the ag acres | 22 | 1.38 | ++
Install Denitrification Bioreactors on all tile drained acres | 18 | 0.92 | 
Install Buffers on all applicable lands | 7 | 1.91 | ++
Installing Controlled Drainage on all applicable acres | 2 | 1.29 | 
Perennial crops (energy crops) on ~6.5 million acres | 18 | 21.46 | ++

## Slide 24: Overall Comparison of Phosphorus Practices
 | P Reduction | Cost of P Reduction | Other Benefits (Ecosystem Services)
Practice/Scenario | % (from baseline) | ($/lb) | 
Cover crops (rye) on ALL CS and CC acres | 50 | 60 | ++
Convert all tillage to no-till | 39 | 14 | ++
P rate reduction in MLRA’s that have high to very high soil test P | 7 | -110 | 
Establish streamside buffers (35ft) on all crop land | 18 | 14 | ++
Perennial crops (energy crops) equal to pasture/hay acreage from 1987 | 29 | 238 | ++
Pasture and Land Retirement to equal acreage of Pasture/Hay and CRP from 1987 | 9 | 120 | ++