## Slide 1: Scenario Analysis
costs per acre for various practices
estimate each fully applied practice for N or P
then combine for N or P to reach 20 or 45%
finally, combine N and P scenarios together

## Slide 2: Nitrogen costs per acre
 | Practice/Scenario | Cost Per Acre | Notes
 | Reducing N rate from background to the MRTN (10% of acres) | -$8 | Reduce N rates (20 pounds)
 | Nitrification inhibitor with all fall applied fertilizer on tile-drained corn acres | $7 | Cost of inhibitor
 | Split (50%) fall and spring (50%) on tile-drained corn acres | $17 | Additional field pass, switch to N solutions
 | Fall to spring on tile-drained corn acres | $18 | Switch to N solutions, higher ammonia price, additional application costs
 | Cover crops on all corn/soybean tile-drained acres | $29 | Aerial applications of cereal rye
 | Cover crops on all corn/soybean non-tiled acres | $29 | Aerial applications of cereal rye
 | Bioreactors on 50% of tile-drained land | $17 | Upfront costs of $133 per acre
 | Wetlands on 25% of tile-drained land | $60 | 5% of farmland out of production Major cost is land ($11,000)
 | Buffers on all applicable crop land (reduction only for water that interacts with active area) | $294 per buffer acre | Land costs plus $50 planting, $10 yearly maintenance
 | Perennial/energy crops equal to pasture/hay acreage from 1987 | $86 | Less profit compared to corn-soybean rotation
 | Perennial/energy crops on 10% of tile-drained land | $86 | Less profit compared to corn-soybean rotation
Edge-of-field
Land use change
In-field

## Slide 3: Phosphorus costs per acre
 | Practice/Scenario | Cost Per Acre | Notes
 | Reduce tillage | -$16 | Eliminate one pass of heavy equipment, no change in yield
 | No P fertilizer on 12.5 million ac of CS fields with soil test P above maintenance level for average of 6 years | -$15 | Cost of six years of P fertilizer averaged over 20 years.
 | Cover crops on corn/soybean tile-drained acres | $29 | Aerial applications of cereal rye
 | Cover crops on corn/soybean non-tiled acres | $29 | Aerial applications of cereal rye
 | Bioreactors on 50% of tile-drained land | $17 | Upfront costs of $133 per acre
 | Wetlands on 25% of tile-drained land | $60 | 5% of farmland out of production Major cost is land ($11,000)
 | Buffers on all applicable crop land (reduction only for water that interacts with active area) | $294 per buffer acre | Land costs plus $50 planting, $10 yearly maintenance
 | Perennial/energy crops equal to pasture/hay acreage from 1987 | $86 | Less profit compared to corn-soybean rotation
 | Perennial/energy crops on 10% of tile-drained land | $86 | Less profit compared to corn-soybean rotation
Edge-of-field
Land use change
In-field
Notes: Costs are all annualized to put on the same basis. Some have substantial first year costs.

## Slide 4: Example Statewide Results for N
 | Practice/Scenario | Nitrate-N reduction per acre (%) | Nitrate-N reduced (million lb N) | Nitrate-N Reduction % (from baseline) | Cost ($/lb N removed)
 | Baseline |  | 410 |  | 
 | Reducing N rate from background to the MRTN (10% of acres) | 10 | 2.3 | 0.6 | -4.25
 | Nitrification inhibitor with all fall applied fertilizer on tile-drained corn acres | 10 | 4.3 | 1.0 | 2.33
 | Split (50%) fall and spring (50%) on tile-drained corn acres | 7.5 to 10 | 13 | 3.1 | 6.22
 | Fall to spring on tile-drained corn acres | 15 to 20 | 26 | 6.4 | 3.17
 | Cover crops on all corn/soybean tile-drained acres | 30 | 84 | 20.5 | 3.21
 | Cover crops on all corn/soybean non-tiled acres | 30 | 33 | 7.9 | 11.02
 | Bioreactors on 50% of tile-drained land | 40 | 56 | 13.6 | 1.38
 | Wetlands on 25% of tile-drained land | 40 | 28 | 6.8 | 5.06
 | Buffers on all applicable crop land (reduction only for water that interacts with active area) | 90 | 36 | 8.7 | 1.63
 | Perennial/energy crops equal to pasture/hay acreage from 1987 | 90 | 10 | 2.6 | 9.34
 | Perennial/energy crops on 10% of tile-drained land | 90 | 25 | 6.1 | 3.18
 | Point source reduction to 10 mg nitrate-N/L |  | 14 | 3.4 | 3.30
 | Point source reduction in N due to biological nutrient removal for P |  | 8 | 1.8 | 
Point source
Edge-of-field
Land use change
In-field
Notes: This table is for nitrate reductions and applies each practice individually for the entire state to a maximum amount. It is useful to see what the impact is and the cost per lb removed. The reductions are not necessarily additive here.

## Slide 5: Example Statewide N Scenarios
Name | Combined Practices and/or Scenarios | Nitrate-N (% reduction) | Total P (% reduction) | Cost of N Reduction ($/lb) | Annualized Costs (million $/year)
N1 | MRTN rate, all spring N application, cover crops 70% tile-drained & 40% non-tiled, bioreactors 50%, wetlands 25%, all ag streams have buffers | 45 | 20 | 3.67 | 678
N2 | MRTN rate, all spring N application, cover crops 100% tile-drained & 70% non-tiled, bioreactors 50%, perennial crops non-tiled, point source to 10 mg nitrate-N/L | 45 | 33 | 4.34 | 811
N3 | MRTN rate, cover crops 100% tile-drained & 65% non-tiled, wetlands 25%, perennial crops non-tiled, all ag streams have buffers, point source to 10 mg nitrate-N/L | 45 | 24 | 4.51 | 833
N4 | MRTN rate, all spring N application, cover crops 5% tile-drained, bioreactors 50% | 20 | 0.3 | 1.99 | 162
N5 | MRTN rate, cover crops 35% tile-drained, bioreactors 50% | 20 | 2 | 2.00 | 161
N6 | MRTN rate, cover crops 75% tile-drained, 50% non-tiled | 20 | 8 | 4.55 | 370
Notes: Here nitrate reduction practices are combined taking into account that one may impact the effectiveness of another. Both 45% and 20% reduction scenarios are presented. The total P reductions shown are what they would be given the N practices. N1 is the cheapest (more bioreactors and wetlands), N2 more cover crops and point source, and N3 includes land use change (perennials).

## Slide 6: Example Statewide Results for P
 | Practice/Scenario | Total P reduction per acre (%) | Total P reduced (million lb P) | Total P Reduction % (from baseline) | Cost ($/lb P removed)
 | Baseline |  | 37.5 |  | 
 | Convert 1.8 million acres of conventional till eroding >T to reduced, mulch or no-till | 50 | 1.8 | 5.0 | -16.60
 | P rate reduction on fields with soil test P above the recommended maintenance level | 7 | 1.9 | 5.0 | -97.50
 | Cover crops on all corn/soybean acres | 30 | 4.8 | 12.8 | 130.40
 | Cover crops on 1.6 million acres eroding>T currently in reduced, mulch or no-till | 50 | 1.9 | 5.0 | 24.50
 | Wetlands on 25% of tile-drained land | 0 | 0 | 0.0 | 
 | Buffers on all applicable crop land | 25-50 | 4.8 | 12.9 | 11.97
 | Perennial/energy crops equal to pasture/hay acreage from 1987 | 90 | 0.9 | 2.5 | 102.30
 | Perennial/energy crops on 1.6 million acres>T currently in reduced, mulch or no-till | 90 | 3.5 | 9.0 | 40.40
 | Perennial/energy crops on 10% of tile-drained land | 50 | 0.3 | 0.8 | 250.07
 | Point source reduction to 1.0 mg total P/L (majors only) |  | 8.3 | 22.1 | 13.71
Point source
Edge-of-field
Land use change
In-field
USLE method
Notes: This table is for total P reductions and applies each practice individually for the entire state to a maximum amount. It is useful to see what the impact is and the cost per lb removed. The reductions are not necessarily additive here.

## Slide 7: Example Statewide P Scenarios
Name | Combined Practices and/or Scenarios | Nitrate-N (% reduction) | Total P (% reduction) | Cost of P Reduction ($/lb) | Annualized Costs (million $/year)
P1 | No P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, buffers on all applicable lands, point source to 1.0 mg TP/L | 6 | 45 | -2.54 | -46
P2 | No P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, cover crops on all CS, point source to 1.0 mg TP/L | 28 | 45 | 31.05 | 521
P3 | No P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, cover crops on 87.5% of CS, buffers on all applicable lands, perennial crops on 1.6 million ac >T, and 0.9 million additional ac. | 37 | 45 | 35.85 | 602
P4 | No P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, buffers on 80% of all applicable land | 5 | 20 | -22.53 | -172
P5 | No P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, point source to 1.0 mg TP/L on 45% of discharge | 0 | 20 | -21.87 | -167
P6 | No P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, cover crops on 1.6 million ac eroding >T and 40% of all other CS | 13 | 20 | 8.80 | 78
Notes: Here total P reduction practices are combined taking into account that one may impact the effectiveness of another. Both 45% and 20% reduction scenarios are presented. The nitrate-N reductions shown are what they would be given the P practices. P1 is the least costly, P2 doesn’t take any cropland out of production, and P3 does not rely on point source reductions.

## Slide 8: Example Statewide N & P Scenarios
Name | Combined Practices and/or Scenarios | Nitrate-N (% reduction) | Total P (% reduction) | Cost of Reduction ($/lb) | Annualized Costs (million $/year)
NP1 | MRTN, fall to spring, bioreactors 50%, wetlands 25%, no P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, buffers on all applicable lands, point source to 1.0 mg TP/L and 10 mg nitrate-N/L | 35 | 45 | ** | 289
NP2 | MRTN, fall to spring, bioreactors 50%, no P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, cover crops on all CS, point source to 1.0 mg TP/L and 10 mg nitrate-N/L | 45 | 45 | ** | 716
NP3 | MRTN, fall to spring, bioreactors 15%, no P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, cover crops on 87.5% of CS, buffers on all applicable lands, perennial crops on 1.6 million ac >T, and 0.9 million additional ac. | 45 | 45 | ** | 697
NP4 | MRTN, fall to spring N, bioreactors 35%, no P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, buffers on 80% of all applicable land | 20 | 20 | ** | -46
NP5 | MRTN, fall to spring N, bioreactors 30%, wetlands 15%, no P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, point source to 1.0 mg TP/L and 10 mg nitrate-N/L on 45% of discharge | 20 | 20 | ** | -28
NP6 | MRTN, fall to spring N, no P fert. on 12.5 million ac above STP maintenance, reduced till on 1.8 million ac conv. till eroding > T, cover crops on 1.6 million ac eroding >T and 40% of all other CS | 24 | 20 | ** | 150
Notes: Here we try to optimize both nitrate-N and total P reduction strategies. Cost per lb can’t really be calculated at this point. NP4 and NP5 save $ because of P changes at the 20% reduction level.

## Slide 9: Agriculture Subcommittee Survey
Practice | Median adoption rate (%) | N reduction (million lb N) | P reduction (million lb P)
Timing change (either fall to spring or fall/spring/side dress) | 65 | 17 | 0
Cover crops – tile drained corn and soybean acres | 25 | 21 | 0.5
Ephemeral gulley control | 65 | ? | ?
Buffers on ag streams | 50 | 13 | 2.4
Wetlands on tile drained acres | 10 | 11 | 0
No P fertilizers with STP above maintenance | 78 | 0 | 1.5
No manure application on frozen ground | 93 | ? | ?
Convert 1.8 million acres of conventional till eroding > T to reduced, mulch, or no till | 60 | 0 | 1.1
Summed |  | 60 (15%) | 5.5 (15%)
Notes: If all these practices were adopted by 2025 there would be about a 15% reduction both nitrate and total P stream loads from agriculture.